## Slide 1
Track Preparation
NN220-06
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation– Updated May 2023
SEANAV I United States Naval Academy

## Slide 2
References
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-The American Practical Navigator, Pub. No. 9, Bowditch, VOL. 1, 2019 Edition -Surface Ship Navigation Department Organizations and Regulations Manual (NAVDORM), COMNAVSURFPAC/COMNAVAIRPAC/COMNAVAIRLANT/COMNAVSURFLANT INSTRUCTION 3530.4 series -Chart Preparation Checklist

## Slide 3
Enabling Objectives
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
1 - DESCRIBE advance and transfer. 2 - FIND a turn point for a given waypoint using an advance and transfer table. 3 - EXPLAIN the use of a slide bar. 4 - LABEL a turn properly with a slide bar and range marks. 5 - DESCRIBE a turn bearing and how they are labeled. 6 - PLOT a turn bearing. 7 - DESCRIBE turn ranges and how they are labeled. 8 - PLOT a turn range. 9 - DESCRIBE how to shift to constants. 10 - EXPLAIN danger bearings. 11 - PLOT a danger bearing.

## Slide 4
NAVKIT
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-Ensure that you have the following instruments: Dividers Compasses Pencils and Erasers (A mechanical pencil is preferred due to the fine edge) Nautical Slide Rule (For quick and easy time, speed and distance calculations) Markers (Green, Yellow, Blue) Fine Edge Black Marker NAVAID Template Chart Correction Template All items should be available in your NAVKIT.

## Slide 5
Chart Preparation Checklist
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy

## Slide 6
Advance and
Transfer
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy

## Slide 7
WP 1
C: 090T/080M
S: 10kts
D: 4,500yds
C: 044T/034M
S: 10kts
D: 4,500yds
600 yards
VA
RB
Advance and Transfer

## Slide 8
Advance is the distance gained in the original directions until vessel steadies on her new course.
Transfer is the distance gained at right angles to the original course until vessel steadies on her new course.
Advance and Transfer are determined based on angle of turn, rudder angle and vessel’s speed. Every vessel has specific tactical data tables which represent turning characteristics based on these factors. Example below:
Turn Point
Steady Point
ANGLE OF TURN
Advance and Transfer

## Slide 9
Vessels are not always on track. Slide Bar assist the navigator in quickly revising a turn bearing if the vessel is off track just prior to a turn. Draw the slide bar parallel to the new course through the turning point of the original course.
Steady Point
Turn Point
VA
TB: “VA” 180T/090R
TB: “Visual Aid” XXXT/XXXR
XXXT = Direction from Turn Point to Turn Aid
XXXR = XXXT – Original Course (If negative number + 360)
TR: “RADAR Aid” XXXX YDS
TR: “RB” 1,000yds
RB
TB: “VA” 190T/100R
corrected
TR: “RB” 900yds
corrected
Turn Point, Slide Bar, and Turn Bearing

## Slide 10: Slide Bar
10
VF
RD
RC
Slide Bar tells when to turn if you are left or right of track.
Left off the track
Right off the track
Turn point
090oT / 077oM
5,950 yds
15kts

## Slide 11
When underway a navigation team is taking fixes at a duration of time. To accurately “mark a turn,” the navigator “shifts to constants” prior to a turn. This means that instead of taking fixes the navigation team will focus solely on the turn/range bearing.
After steadying on new course the navigation team will resume taking fixes.
VA
TB: “VA” 180T/090R
“VA” 165T
“VA” 150T
“VA” 135T
0800
0803
“Shifting to Constants”
“Mark Turn”
500
300
400
200
100
Select a Turn Bearing as close as possible off your beam. This will create the greatest rate of change of bearing and will result in a more precise turn. When selecting a Turn Range, select a RADAR aid as close to as possible off your bow/stern.
Turn Point, Slide Bar, and Turn Bearing

## Slide 12: Determine Turn Bearing
Visual NAVAIDs off the beam will have a more rapid bearing change
and will provide a more precise LOP with which to mark your turn.
VB/RB
VC/RC
VD/RD
VA/RA
Best for
Turn Bearing
Bearing changes largely enough to know the exact timing to mark turn.
Bearing changes too slightly to know the exact timing to mark turn.
Bad for
Turn Bearing

## Slide 13: Determine Turn Range
13
Radar NAVAIDs off the bow will have a more rapid range change and will provide a more precise LOP with which to mark your turn.
VB/RB
VC/RC
VD/RD
VA/RA
You
Best for
Turn Range
Range changes too slightly to know the exact timing to mark turn.
Range changes largely enough to know the exact timing to mark turn.
Bad for
Turn Range

## Slide 14: How to determine Advance & Transfer? (1/6)
14
Use “Advance & Transfer Table”, which varies by ship type.
SPEED | RUDDER | Angle of Turn from current to new course |  |  |  |  |  |  |  |  |  |  | 
 |  |  | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55
5 | 15 | A | 83 | 167 | 250 | 306 | 360 | 415 | 468 | 520 | 575 | 620 | 657
 |  | T | 3 | 6 | 15 | 27 | 42 | 60 | 83 | 105 | 135 | 162 | 189
8 | 15 | A | 85 | 171 | 256 | 310 | 362 | 418 | 469 | 524 | 575 | 620 | 659
 |  | T | 3 | 5 | 9 | 17 | 29 | 48 | 67 | 93 | 126 | 150 | 181
9 | 15 | A | 86 | 173 | 258 | 312 | 362 | 419 | 469 | 256 | 575 | 621 | 660
 |  | T | 2 | 5 | 7 | 14 | 24 | 44 | 61 | 89 | 123 | 146 | 178
10 | 15 | A | 87 | 173 | 260 | 313 | 363 | 420 | 470 | 527 | 575 | 621 | 661
 |  | T | 2 | 4 | 5 | 11 | 20 | 40 | 56 | 85 | 120 | 142 | 175
11 | 15 | A | 89 | 176 | 260 | 312 | 362 | 416 | 465 | 422 | 567 | 614 | 654
 |  | T | 2 | 5 | 9 | 15 | 25 | 44 | 61 | 90 | 125 | 148 | 181
12 | 15 | A | 90 | 179 | 260 | 311 | 361 | 412 | 460 | 417 | 559 | 607 | 647
 |  | T | 2 | 6 | 13 | 19 | 30 | 48 | 66 | 95 | 130 | 153 | 187
13 | 15 | A | 92 | 181 | 260 | 310 | 359 | 408 | 456 | 412 | 551 | 601 | 639
 |  | T | 2 | 8 | 17 | 24 | 35 | 52 | 70 | 100 | 135 | 159 | 194
14 | 15 | A | 93 | 184 | 260 | 309 | 358 | 404 | 451 | 407 | 543 | 594 | 632
 |  | T | 3 | 9 | 21 | 28 | 40 | 56 | 75 | 105 | 140 | 164 | 200
15 | 15 | A | 95 | 187 | 260 | 308 | 357 | 400 | 446 | 502 | 535 | 587 | 625
 |  | T | 3 | 10 | 25 | 32 | 45 | 60 | 80 | 110 | 145 | 170 | 206
Speed
Rudder Angle
Amount of Turn from current to new course

## Slide 15: How to determine Advance & Transfer? (2/6)
15
Q1: What are Advance and Transfer if you turn at 15kts with standard rudder from 090°T to 137°T?
SPEED | RUDDER | Angle of Turn from current to new course |  |  |  |  |  |  |  |  |  |  | 
 |  |  | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55
14 | 15 | A | 93 | 184 | 260 | 309 | 358 | 404 | 451 | 407 | 543 | 594 | 632
 |  | T | 3 | 9 | 21 | 28 | 40 | 56 | 75 | 105 | 140 | 164 | 200
15 | 15 | A | 95 | 187 | 260 | 308 | 357 | 400 | 446 | 502 | 535 | 587 | 625
 |  | T | 3 | 10 | 25 | 32 | 45 | 60 | 80 | 110 | 145 | 170 | 206
5 | 30 | A | 55 | 110 | 165 | 202 | 235 | 275 | 307 | 335 | 365 | 392 | 417
 |  | T | 0 | 0 | 0 | 6 | 11 | 20 | 29 | 38 | 50 | 63 | 78
8 | 30 | A | 41 | 82 | 123 | 149 | 175 | 203 | 225 | 246 | 266 | 286 | 303
 |  | T | 1 | 3 | 6 | 10 | 16 | 23 | 37 | 48 | 65 | 178 | 92
1) Find your speed, rudder angle and Amount of Turn on the table.
2) Advance and Transfer for 47° turn should be between the ones of 45° and 50°.
Advance:
47°
137°- 090°
45°
535(yds)
50°
587(yds)
47°
? (yds)

## Slide 16: How to determine Advance & Transfer? (3/6)
16
Q1: What are Advance and Transfer if you turn at 15kts with standard rudder from 090°T to 137°T?
3) Determine Advance for 47° turn.
535 + (587 – 535 ) / (50 – 45)*2 = 535 + 10.4*2 = 555.8 (yds)
4) Determine Transfer for 47° turn in same way as for Advance.
145 + (170 – 145) / (50-45)*2 = 145 + 5*2
= 155 (yds)
SPEED | RUDDER | Angle of Turn from current to new course |  |  |  |  |  |  |  |  |  |  | 
 |  |  | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55
14 | 15 | A | 93 | 184 | 260 | 309 | 358 | 404 | 451 | 407 | 543 | 594 | 632
 |  | T | 3 | 9 | 21 | 28 | 40 | 56 | 75 | 105 | 140 | 164 | 200
15 | 15 | A | 95 | 187 | 260 | 308 | 357 | 400 | 446 | 502 | 535 | 587 | 625
 |  | T | 3 | 10 | 25 | 32 | 45 | 60 | 80 | 110 | 145 | 170 | 206
5 | 30 | A | 55 | 110 | 165 | 202 | 235 | 275 | 307 | 335 | 365 | 392 | 417
 |  | T | 0 | 0 | 0 | 6 | 11 | 20 | 29 | 38 | 50 | 63 | 78
8 | 30 | A | 41 | 82 | 123 | 149 | 175 | 203 | 225 | 246 | 266 | 286 | 303
 |  | T | 1 | 3 | 6 | 10 | 16 | 23 | 37 | 48 | 65 | 178 | 92
Advance per 1 °
Transfer per 1 °

## Slide 17: How to determine Advance & Transfer? (4/6)
17
SPEED | RUDDER | Angle of Turn from current to new course |  |  |  |  |  |  |  |  |  |  | 
 |  |  | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55
5 | 15 | A | 83 | 167 | 250 | 306 | 360 | 415 | 468 | 520 | 575 | 620 | 657
 |  | T | 3 | 6 | 15 | 27 | 42 | 60 | 83 | 105 | 135 | 162 | 189
8 | 15 | A | 85 | 171 | 256 | 310 | 362 | 418 | 469 | 524 | 575 | 620 | 659
 |  | T | 3 | 5 | 9 | 17 | 29 | 48 | 67 | 93 | 126 | 150 | 181
9 | 15 | A | 86 | 173 | 258 | 312 | 362 | 419 | 469 | 256 | 575 | 621 | 660
 |  | T | 2 | 5 | 7 | 14 | 24 | 44 | 61 | 89 | 123 | 146 | 178
10 | 15 | A | 87 | 173 | 260 | 313 | 363 | 420 | 470 | 527 | 575 | 621 | 661
 |  | T | 2 | 4 | 5 | 11 | 20 | 40 | 56 | 85 | 120 | 142 | 175
11 | 15 | A | 89 | 176 | 260 | 312 | 362 | 416 | 465 | 422 | 567 | 614 | 654
 |  | T | 2 | 5 | 9 | 15 | 25 | 44 | 61 | 90 | 125 | 148 | 181
12 | 15 | A | 90 | 179 | 260 | 311 | 361 | 412 | 460 | 417 | 559 | 607 | 647
 |  | T | 2 | 6 | 13 | 19 | 30 | 48 | 66 | 95 | 130 | 153 | 187
13 | 15 | A | 92 | 181 | 260 | 310 | 359 | 408 | 456 | 412 | 551 | 601 | 639
 |  | T | 2 | 8 | 17 | 24 | 35 | 52 | 70 | 100 | 135 | 159 | 194
14 | 15 | A | 93 | 184 | 260 | 309 | 358 | 404 | 451 | 407 | 543 | 594 | 632
 |  | T | 3 | 9 | 21 | 28 | 40 | 56 | 75 | 105 | 140 | 164 | 200
15 | 15 | A | 95 | 187 | 260 | 308 | 357 | 400 | 446 | 502 | 535 | 587 | 625
 |  | T | 3 | 10 | 25 | 32 | 45 | 60 | 80 | 110 | 145 | 170 | 206
Q2: What are Advance and Transfer if you turn at 9kts with standard rudder from 090°T to 113°T?

## Slide 18: How to determine Advance & Transfer? (5/6)
18
Q2: What are Advance and Transfer if you turn at 9kts with standard rudder from 090°T to 113°T?
SPEED | RUDDER | Angle of Turn from current to new course |  |  |  |  |  |  |  |  |  |  | 
 |  |  | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55
9 | 15 | A | 86 | 173 | 258 | 312 | 362 | 419 | 469 | 256 | 575 | 621 | 660
 |  | T | 2 | 5 | 7 | 14 | 24 | 44 | 61 | 89 | 123 | 146 | 178
1) Find your speed, rudder angle and Amount of Turn on the table.
2) Advance and Transfer for 23° turn should be between the ones of 20° and 25°.
Advance:
23°
113°- 090°
20°
312(yds)
25°
362(yds)
23°
? (yds)

## Slide 19: How to determine Advance & Transfer? (6/6)
19
Q2: What are Advance and Transfer if you turn at 9kts with standard rudder from 090°T to 113°T?
3) Determine Advance for 23° turn.
312 + (362 – 312 ) / (25 – 20)*3 = 312 + 10*3
4) Determine Transfer for 23° turn in same way as for Advance.
14 + ( 24 – 14) / (25 – 20)*3 = 14 + 2*3
SPEED | RUDDER | Angle of Turn from current to new course |  |  |  |  |  |  |  |  |  |  | 
 |  |  | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55
9 | 15 | A | 86 | 173 | 258 | 312 | 362 | 419 | 469 | 256 | 575 | 621 | 660
 |  | T | 2 | 5 | 7 | 14 | 24 | 44 | 61 | 89 | 123 | 146 | 178
= 342 (yds)
= 20 (yds)

## Slide 20
Plot a Slide Bar and Range Marks
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy

## Slide 21
90
270
90
270
90
270
1,200 yds
VA
VB
RA
RD
RC
VC
090°T / 078°M
6 kts
124°T / 112°M
3,200 yds
6 kts
Transfer
Transfer
Advance
50
100
200
300
400
500
600
700
800

## Slide 22
Turn Bearing / Turn Range
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy

## Slide 23
160
340
1,200 yds
VA
VB
RA
RD
RC
VC
090°T / 078°M
6 kts
124°T / 112°M
3,200 yds
6 kts
TB:“VA” 340°T / 250°R
TR:“RC” 1,900 yds
50
Turn bearings are ideal off the beams, where bearing change happens quickly
Turn ranges are ideal off the bow or stern, where range change happens quickly

## Slide 24
VB
600 yards
VA
DB: “VB” _____ 100T
“VA” 095T
“VA” 105T
NLT
Danger Bearings are used by the navigator to keep clear of an area of danger close to which the vessel must pass. It is established between two fixed objects (danger area and navigation aid). The navigation aid should be in the same general direction of the course when passing the danger.
Danger Bearing

## Slide 25
Approach Track is defined as the track that a vessel must make good in order to arrive at the center of her assigned berth.
Head Bearing (HB) is a bearing to a visual aid from the approach track. The anchorage point should be chosen by finding a HB that will exactly match the approach course. If you don’t have a HB, move the anchorage point or change the course!
HB: “VA” 090T/080M
Anchorage Plotting
1,000 yds
090°T / 078°M
6 kts

## Slide 26
The let-go-bearing (LGB) is a bearing to a visual aid from the point of intersection of the LGC and approach track.
Since the location where the navigator is taking bearing from is not the same location that the anchor is let go, the letting-go-circle (LGC) is drawn around the planned anchorage. LGC = distance between the hawsepipe and the pelorus.
Hawsepipe to Peloris
LGC
LGB: “VB” 185T/095R
“Let Go Anchor”
Anchorage Plotting

## Slide 27
Drag Circle is plotted from the actual anchorage position as the center and the radius is equal to the sum of the distance of the hawespipe to pelorus and the amount of anchor chain let out rounded to the next whole shot. All fixes following anchorage should fall within this circle or the anchor is dragging. HAWSEPIPE TO PELORUS + LENGTH OF CHAIN = DRAG CIRCLE
Swing Circle is plotted from the actual anchorage position as the center and the radius is equal to the sum of the distance of the length of ship and the amount of anchor chain let out. Its purpose is to ensure the ship will be in safe water while anchored. LENGTH OF CHAIN + LENGTH OF SHIP = SWING CIRCLE
Anchorage Plotting

## Slide 28
80 85 S 75 S 72 65
55 46 M 44
S 40 41
33 39 M 40 M
Co 38 40
VA
Anchorage Plotting
1,200 yards
VB
SHIP’S CHARACTERISTICS:
Ship Length: 300 feet
Hawespipe to Pelorus: 100 feet
HB: “VA” 130T/120M
LGB: “VB” 220T/090R
LGC
-Depth of Water: Required to let out 5-7 x depth of water
-Bottom Type: Mud, Sand are ideal
-Traffic Density: Away from heavy traffic
-Safe for Navigation: When anchored the swing circle (length of chain + length of ship) falls in safe waters
-Identify navaid to use as HB and another for use as LGB. HB is in Degrees True and Magnetic. Ensure Approach Track and HB match!
-Measure and plot the radius of the letting-go circle (Hawespipe to Pelorus) over center of anchorage.
-Scribe and lable the range arcs on chart (100-1000, 1200, 1500, 2000 yds) starting from the LGC.
-Plot and label LGB from the LGC to the applicable navaid. Degrees True and Relative!
C: 130T/120M
D: 1,000 yds
500
200
300
400
100
C: 090T/080M
S: 10 kts
D: 5,000 yds

## Slide 29
VA
Anchorage Plotting
1,200 yards
VB
SHIP’S CHARACTERISTICS:
Ship Length: 300 feet
Hawespipe to Pelorus: 100 feet
Anchor
Following anchorage plot drag and swing circle. Take 3 consecutive fixes ensuring they fall within the drag circle.
0800
0803
0806
If a fix plots outside the drag circle then you are dragging anchor. Raise the anchor and then try to anchor again.
Drag
Swing
Only plot the swing/drag circles AFTER you anchor. In other words, DO NOT prep your chart with the swing and drag circle already plotted

## Slide 30
Enabling Objectives
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
1 - DESCRIBE advance and transfer. 2 - FIND a turn point for a given waypoint using an advance and transfer table. 3 - EXPLAIN the use of a slide bar. 4 - LABEL a turn properly with a slide bar and range marks. 5 - DESCRIBE a turn bearing and how they are labeled. 6 - PLOT a turn bearing. 7 - DESCRIBE turn ranges and how they are labeled. 8 - PLOT a turn range. 9 - DESCRIBE how to shift to constants. 10 - EXPLAIN danger bearings. 11 - PLOT a danger bearing.

## Slide 31
Questions?
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy