## Slide 1
Dead Reckoning and Piloting
NN220-07
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation– Updated May 2023
SEANAV I United States Naval Academy

## Slide 2
References
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-The American Practical Navigator, Pub. No. 9, Bowditch, VOL. 1, 2019 Edition -Surface Ship Navigation Department Organizations and Regulations Manual (NAVDORM), COMNAVSURFPAC/COMNAVAIRPAC/COMNAVAIRLANT/COMNAVSURFLANT INSTRUCTION 3530.4 series

## Slide 3
Enabling Objectives
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
1 - DEFINE Piloting. 2 - DESCRIBE the steps needed to prepare the plotting station. 3 - IDENTIFY the applicable records book needed to record plotting information. 4 - UNDERSTAND how to determine Gyrocompass Error. 5 - IDENTIFY the critical watchstanders needed to transition to restricted waters transit IAW the NAVDORM. 6 - DESCRIBE Visual Fix and demonstrate how a plotter fixes and labels a position using visual NAVAIDs. 7 - DESCRIBE RADAR Fix and demonstrate how a plotter fixes and labels a position using RADAR NAVAIDs. 8 - DESCRIBE COMPOSITE Fix and demonstrate how a plotter fixes and labels a position using both Visual and RADAR NAVAIDs. 9 - DESCRIBE GPS Fix and demonstrate how a plotter fixes and labels a position using GPS. 10 - DESCRIBE Estimated Position and demonstrate how a plotter fixes and labels it. 11 - DESCRIBE Running Fix and its application in piloting. 12 - EXPLAIN the required fix intervals IAW Table 3-A. 13 - DEFINE Dead Reckoning (DR). 14 - IDENTIFY the Six Rules of Dead Reckoning. 15 - DEMONSTRATE how to properly plot and label the course line and DR positions. 16 - DEFINE Set and Drift and demonstrate how to calculate it. 17 - DEFINE Course Made Good (CMG) and Speed Made Good (SMG) and demonstrate how to determine it. 18 - DESCRIBE Compensating Course and demonstrate how to determine it. 19 - DESCRIBE Correcting Course and demonstrate how to determine it.

## Slide 4
NAVKIT
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-Ensure that you have the following instruments: Dividers Compasses Pencils and Erasers (A mechanical pencil is preferred due to the fine edge) Nautical Slide Rule (For quick and easy time, speed and distance calculations) Markers (Green, Yellow, Blue) Fine Edge Black Marker NAVAID Template Chart Correction Template All items should be available in your NAVKIT.

## Slide 5
Piloting
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Piloting-Involves navigating a vessel in restricted waters and fixing its position as precisely as possible at frequent intervals. -Intervals are in accordance with the NAVDORM, Table 3-A. -The navigator will assign watchstanders to roles to assist in piloting. -Proper preparation and attention to detail is critical during this phase!

## Slide 6
Prepare the Plotting Station
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
We must get prepared to navigate in restricted waters long before we get underway. Ensure you have completed the following:
Have your NAVKIT ready.
Assemble all your charts and publications.
Make sure you have prepared your charts IAW the chart preparation checklist.
Ensure you have all the record books needed (Bearing Book, Position Log, Deck Log, etc)
Verify tides, currents and weather.
Conduct a Navigation/Transit Brief

## Slide 7
Record Books
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-Chapter 6 of the NAVDORM covers all the record books, logs and forms needed for a US Navy warship. -Ship’s Deck Log-Maintained as a complete daily record of all important events which may affect the crew, safety of the ship or has historical value. -Ship’s Position Log-Record of all positions and sounding from all sources used, including GPS and fathometer sounding. -Standard Bearing Book-Record of the data obtained to determine the ship’s position by visual bearings, sextant angles, RADAR bearings or RADAR ranges. -Navigation Workbook-Record of all observations and computations used for the navigation of the ship.

## Slide 8
Record Books
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-Chapter 6 of the NAVDORM covers all the record books, logs and forms needed for a US Navy warship. -RADAR Navigation Log-Sometimes called a navigational fix log, is used whenever RADAR navigation is conducted. -Chart and Publications Corrections-record of all corrections required for the current allowance of NGA charts, DNCs, ENCs and publications established by the current edition of the Nautical Chart and Publications Allowance. -Notice to Mariners and Summary of Corrections-A series of publications that incorporates a historic record of corrections dating from the most recent edition date for NGA products back to July 1975.

## Slide 9
Gyrocompass Error
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Gyrocompass-A non-magnetic compass based on a fast-spinning disc and the rotation of the Earth that finds true north. -Used by bearing takers to take bearings to NAVAIDs. -The total of all the combined errors of the gyrocompass is called Gyro Error. This error will affect the bearings taking during piloting. -Expressed in East or West, just like variation and deviation. -To find Gyro Error, compare the charted bearing to a known object from your position to the Gyrocompass bearing. -If “Gyro is Best” Error is West, If “Gyro is Least” Error is East.

## Slide 10
Watchstanders
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-The NAVDORM dictates the required watchstations for the different phases of navigation.
-Requirements will be different for different platforms.
-The critical watchstations will include:
Navigation Evaluator
Navigation Plotter/ECDIS-N Operator
Bearing Takers
Navigation RADAR Operator
Bearing Recorder

## Slide 11
Fix Symbology
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
- All fixes plotted on the chart will be represented by a symbol and labeled with the four digit time corresponding to when it was taken (ex. 1600)

## Slide 12
Lines of
Position
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
- Probably the most important and elemental concept in navigation;
- Whereas an exact position is a point on a chart, an LOP is a line, along which the navigator knows he or she is located. It is measured from a NAVAID;
- A minimum of two LOPs is needed for a fix, and three or more LOPs yield a more reliable fix (3 LOPs required IAW NAVDORM);
- Can be obtained in many ways, but in piloting the 2 primary means are:
a) Visual – bearing of a known, fixed object through the use of the pelorus or gyro repeater; and
b) RADAR – range (distance) to a known object through the use of the ship’s radar.

## Slide 13
Lines of
Position
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Visual bearings are nearly always preferable to radar bearings. You are less likely to make an error if you can see the object rather than trusting that the electronic image you are using is the same one you think it is;
You must exercise some judgment in choosing the objects you will use for your bearings. Most important:
=> the objects must appear on the chart; and
=> choose objects that will yield bearings that are widely spread.
- If you have multiple LOPs to take:
Visual - “Beam, Bow, Stern” → Should avoid shooting anything on the stern as there is no appreciable bearing change.
RADAR - “Bow, Stern, Beam” → Should avoid shooting anything on the beam as there is no appreciable range change.

## Slide 14
Visual Lines of
Position
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
- Visual LOPs are represented by a straight line towards a fixed object (visual NAVAID); and
- It is read from the center of the object; and
- It is labeled with the time (mandatory) and the direction (option).
* Notice that the line you are drawing is actually the reciprocal of the bearing you took on the object, since you are drawing it from the observed object rather than to it.

## Slide 15
Optimum Spread of Visual LOPs
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
- Prevents the bearings from being too close together and helps provide a more precise fix;
- The optimum spread for LOP’s is 120°; and
- If all NAVAIDs are on the same side of the ship, they should be 60° apart.

## Slide 16
Fl R 4 sec
Tank
TWR
1412
3 aids = 120°
120

## Slide 17
TWR
TANK
LT
60
60
0930
Same side = 60°

## Slide 18
Visual Fix
A Visual fix is a position of your vessel on the chart; and
It is obtained based on a combination of 3 visual lines of position.
VR bears 255°
VH bears 316°
VP bears 207°
Intersection of the 3 LOPs is the position of your ship (fix)!

## Slide 19
How to draw LOPs without Compass Rose
VR Bears 240°T

## Slide 20
RADAR Lines of
Position
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
- RADAR LOPs are represented by a range arc line towards a conspicuous RADAR object (RADAR NAVAID); and
- It is read from the leading edge of the object; and
- It is labeled with the time (mandatory) and the range (option).
* Notice that your dividers will create a curved line when you draw the LOP from the RADAR NAVAID.

## Slide 21
RADAR Lines of
Position
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Radar image shows distinct objects on water and the coast contour.
Radar will not show objects on land!

## Slide 22
Triton Light is at a range of 500 yards… This is a RADAR LOP!

## Slide 23
RADAR Fix
A RADAR fix is a position of your vessel on the chart; and
It is obtained based on a combination of 3 RADAR lines of position.
RL is 600 yards
RH is 500 yards
RI is 550 yards.
Intersection of the 3 LOPs is the position of your ship (fix)!

## Slide 24
Composite Fix
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
- Composite Fixes are fixes by both RADAR and Visual Lines of Position.
- It will be marked as an Electronic Fix.
- It is labeled with the time (mandatory).

## Slide 25
GPS Fix
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
- GPS fixes are positioned from a GPS receiver.
- It can also be attained from other GNSS systems.
- The US Navy requires GPS systems that are encrypted.
Read as Latitude/Longitude
Example:
Riverside Observatory coordinates:
- Lat. = 33°57’ 12’’ N
- Long. = 117°23’ 46’’ W
Remember:
1°= 60’ (minutes)
1’ = 60’’ (seconds)
LATITUDE
LONGITUDE

## Slide 26
How to plot GPS Fix
38°58’ 20’’ N / 076°27’ 40’’ W

## Slide 27
Estimated Position
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
- An Estimated Position (EP) is the most probable position of a craft determined from incomplete data or data of questionable accuracy.
- Can be determined by applying a correction to a DR position, accounting for set and drift or by plotting lines of position of questionable accuracy.
- It is commonly gained from plotting two lines of position.

## Slide 28
Estimated Position
Based on Set and Drift
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy

## Slide 29
C - 090°
S - 6 kts
0830
0833
0836
0833
0836
Set & Drift
CMG & SMG
CMG & SMG
If you continue on the same ordered course and speed where do you estimate to be at 0836?
C - 090°
S - 6 kts
0836
0839
Use your CMG and SMG to plot an EP!
Estimated Position

## Slide 30
Estimated Position Based on Single LOP
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy

## Slide 31
Running Fixes
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
- A method for determining the ship’s position with visual LOP’s when only one object is visible.
-Use the following method:
Plot a bearing to a NAVAID (LOP 1).
Plot a second bearing to the same NAVAID at a later time (LOP 2).
Plot a third bearing to the same NAVAID at a later time (LOP 3).
Advance LOP 1 and LOP 2 to the time that LOP 3 was taken.
The intersection of the three LOPs is a running fix!

## Slide 32
Running Fixes
TANK
0800
C 080
S 10
0803
0806
0809
Now, I can see only a TANK!
Time to take 3 LOPs
0809
0806
0803
Got a fix!
Dead Reckoning!
Attempt to get
0809 Running Fix
Advance Parallel, For predicted distance
in 10kt, 6min(0803-0809)
Advance Parallel, For predicted distance
in 10kt, 3min(0806-0809)
0809 RFIX
0812
0815
Notes: Running Fix: Done when only 1 navigation aid is available. Completed by taking 3 fixes over successive fix intervals based on your DRs.

## Slide 33
Dead Reckoning
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
The process of estimating your ship’s future position without considering the effects of wind and current. Based on the ship’s ordered course and speed.
Can help you:
Determine if the current ordered course and speed are safe
Determine when to make course changes or to compute time left on the present course
Determine when to adjust speed
Predict the time of sighting lights and other aids to navigation
Identify landmarks
Determine which navigation aids will provide the best fix
Determine the effects of wind and current on the vessel
Estimate the ship’s position for celestial navigation computations
Determine the validity of a fix

## Slide 34
Dead Reckoning
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy

## Slide 35
Six Rules of Dead Reckoning
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Plot a DR position…
1. At least every hour on the hour while in open ocean
2. At every course change
3. At every speed change
4. After every fix or running fix
5. When obtaining a single line of position (LOP)
6. Label each fix with course, speed, time, and draw a new course line from each fix or running fix. The DR plot should cover at least the next two fix intervals.

## Slide 36
1) Every Hour on the Hour
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
This rule ensures there is a minimum DR interval for every navigator to DR at least every hour.

## Slide 37
2) Every Course Change
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy

## Slide 38
3) Every Speed Change
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
After you change speed, you are no longer going to be where you predicted based on your previous speed.

## Slide 39
4) After a Single LOP
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy

## Slide 40
5) After Every Fix or Running Fix
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy

## Slide 41
6) Draw a New Course Line From Your Fix and DR Out
Two Fix Intervals
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy

## Slide 42
Time/Speed/Distance
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
D = S x T
where: D = distance traveled in nautical miles (nm)
S = speed in knots
T = time in hours

## Slide 43
Speed Wheel
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy

## Slide 44
Three Minute Rule
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
The distance of travel of a ship in yards in
three minutes is equal to its speed in knots multiplied by 100.
D = S x 100
where: D = distance traveled (yards)
              S = speed (knots)

## Slide 45
Six Minute Rule
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
The distance of travel of a ship in nautical miles in six minutes is equal to its speed in knots divided by 10.
D = S / 10
where: D = distance traveled (nm)
              S = speed (knots)

## Slide 46: Practice on Chartlet Plot the First Fix
Date | RC | VH | RF |  | Depth
Time |  |  |  |  | 
0900 | 300yds | 154 | 1200yds |  | 18ft
Notes: Teaching Points:
Read along the Meridian
Visual Fixes are circles
Optimal spread of LOP
When should we take another fix based on the water we are in? (NAVDORM)
After every fix we need to DR…Leads you into Dead Reckoning
  Purpose
  6 Rules
  How to plot….leads into 3 min rule

## Slide 47: Practice on Chartlet Plot DR for First Fix
Ordered Course: 126T
Ordered Speed: 6kts
What information does this DR provide?

## Slide 48: Practice on Chartlet Plot DR for the First Fix
0900
03
06
C 126
S 6

## Slide 49: Practice on Chartlet Plot the Second Fix and DR
Date | RC | VH | RF |  | Depth
Time |  |  |  |  | 
0900 | 300yds | 154 | 1200yds |  | 18
 | VE | VR | VI |  | 
0903 | 281 | 190 | 111 |  | 12
Ordered Course: 126T
Ordered Speed: 6kts
What information does this DR provide?
Notes: Teaching Points:
Read along the Meridian
Visual Fixes are circles
Optimal spread of LOP
When should we take another fix based on the water we are in? (NAVDORM)
After every fix we need to DR…Leads you into Dead Reckoning
  Purpose
  6 Rules
  How to plot….leads into 3 min rule

## Slide 50: Practice on Chartlet Plot the Second Fix and DR
0900
0903
0906
C 126
S 6
0903
0906
0909
C 126
S 6

## Slide 51: Current Triangle
Set: The direction toward which current is flowing.
Drift: The speed of the current.
0000
15
0015
30
C: 090T
S: 10 kts
Current 🡺 resultant of all offsetting influences!!!
CMG/SMG
Current (Set/Drift)
DR (ordered CSE/SPD)
Offsetting influences: tidal current, winds, effect of the winds on the ship itself, heavy seas, inaccurate steering, error in engine calibration...

## Slide 52: Calculate Set and Drift
DR and fix have to be at same time!!!
To calculate Set
Draw a line from the DR to the second fix
Place slide ruler on the line and transpose over to the compass rose
Read the direction off the compass rose in the direction of the line
To calculate Drift
Measure the distance between the DR and the second fix
Divide that distance by time as an application of: S = D / T
CMG
Set

## Slide 53: Practice on Chartlet Calculate Set and Drift for 0903 fix
0900
0903
0906
C 126
S 6
0903
0906
0909
C 126
S 6
Set: 107T
Drift: 2.5 knots
Set / Drift

## Slide 54: Practice on Chartlet Calculate Set and Drift for 0903 fix
90
270
180
360
0
180
100
290
110
280

## Slide 55: Current Triangle
Ordered Course: The course which is ordered and is steered by the helmsman.
Ordered Speed: The speed which is ordered and is controlled by the lee-helmsman.
Course Made Good (CMG): resultant direction from a given point to a subsequent position, disregarding any intermediate course change;
Speed Made Good (SMG): speed based on distance of passage from a given point to a subsequent position;
Track Made Good (SMG): Combination CMG + SMG

## Slide 56: Current Triangle
CMG and SMG is always measured between 2 known positions!!!

## Slide 57: Calculate CMG and SMG
CMG and SMG always between 2 known positions!!!
To calculate CMG
Draw a line from the first fix to the second fix
Place slide ruler on the line and transpose over to the compass rose
Read the direction off the compass rose in the direction of the line
To calculate SMG
Measure the distance between the first fix and the second fix
Divide that distance by time as an application of S = D / T
Fix #1
Fix #2
DR
CMG

## Slide 58: Practice on Chartlet Calculate CMG/SMG for 0903 fix
0900
0903
0906
C 126
S 6
0903
0906
0909
C 126
S 6
CMG – 120T
SMG - 8.1 knots
CMG / SMG

## Slide 59: Practice on Chartlet Plot 3rd Fix and DR
Date | RC | VH | RF |  | Depth
Time |  |  |  |  | 
0900 | 300yds | 154 | 1200yds |  | 18
 | VE | VR | VI |  | 
0903 | 281 | 190 | 111 |  | 12
 |  | VQ | RF |  | 
0906 | 294 | 082 | 440 yds |  | 20
Ordered Course: 155T
Ordered Speed: 4kts

## Slide 60: Practice on Chartlet Plot 3rd Fix and DR
Ordered Course: 155T
Ordered Speed: 4kts
0906
0909
0912
C-155
S- 4

## Slide 61: Practice on Chartlet Plot 4th Fix
Date | RC | VH | RF |  | Depth
Time |  |  |  |  | 
0900 | 300yds | 154 | 1200yds |  | 18
 | VE | VR | VI |  | 
0903 | 281 | 190 | 111 |  | 12
 |  | VQ | RF |  | 
0906 | 294 | 082 | 440 yds |  | 20
 |  |  | VH |  | 
0909 | 300 | 053 | 257 |  | 12

## Slide 62: Practice on Chartlet Plot 4th Fix
0906
0909
0912
C-155
S-4
0909
Ordered Course: 155T
Ordered Speed: 4kts
0912
0915
C-155
S-4

## Slide 63: Practice on Chartlet Calculate Set and Drift
Set: 087 T
Drift: 2kts
0909
0912
0909
0912
0915
C-155
S-4
C-155
S -4

## Slide 64: Practice on Chartlet Calculate CMG and SMG
CMG: 136T
SMG: 5 kts
0909
0912
0909
0912
0915
C-155
S-4
C - 155
S - 4

## Slide 65: Practice on Chartlet Estimate your Position at 0912
0912
0909
0912
0909
0912
0915
C-155
S-4
C - 155
S - 4

## Slide 66: What should you do?
0912
0909
0912
0909
0912
0915
Current is deviating your ship from original track. What should you do?
1 – Regain track → Correcting Course
2 – Make good the intended track → Compensating Course
0906
C - 155
S - 4
C - 155
S- 4

## Slide 67
0900
0903
C-090
S- 10
Set & Drift
0903
0906
0906
0909
D1
D2
Direction From DR(D1) to FIX:
Set
Distance From DR(D1) to FIX:
Drift
(190°)
(300yds / 3min)
190° 300yds
(3kts)
Ordered Course & Speed
Course Made Good Speed Made Good
Actual Track
090oT / 081oM
10 kts
12,000 yds
Set & Drift
C-090
S- 10

## Slide 68
Calculate Compensating Course and Speed
0909
If you don’t alter your course, the position after 3 minutes will be…
Direction From FIX to DR(D2):
Distance From FIX to DR(D2):
(073°)
(1,100yds / 3min)
(11kts)
D1
D2
073° 1,100yds
0900
0903
0906
0909
0903
0906
190° 300yds
Co / Sp Made Good :
090° 10kts
Compensating is… Co/Sp in order to compensate for the actual current (Set & Drift).
090oT / 081oM
10 kts
12,000 yds
0909
Set / Drift
Compensating Co/Sp
×
×
C-090
S- 10
C-090
S- 10

## Slide 69
0900
0903
Calculate Correcting Course and Speed
0903
0906
0906
0909
(060°)
(1,280yds / 3min)
(12.8kts)
D1
D2
060° 1,280yds
190° 300yds
190° 300yds
090oT / 081oM
10 kts
12,000 yds
0906
Correcting is… effectively bringing you back to the second DR of your first fix (D2).
If you don’t alter your course, the position after 3 minutes will be…
Direction From D3 to DR(D2):
Distance From D3 to DR(D2):
D3
Set & Drift
Correcting Co/Sp
C-090
S- 10
C-090
S- 10

## Slide 70
0900
0903
Current Triangle
0903
0906
0906
0909
D1
D2
From DR(D1) to FIX :
Set & Drift
(190° 3kts)
From FIX to DR(D2) :
Compensating
(073°11kts)
From D3 to DR(D2) :
Correcting
(060°12.8kts)
D3
Set & Drift
Correcting
Compensating
C-090
S- 10
C-090
S- 10

## Slide 71: Compensating Course
0912
0909
0912
0909
0912
C 155
S 4
C 155
S 4
Compensating Course / Speed
What is the compensating course and speed for the 0909 fix?
175ºT / 4.1 knots

## Slide 72: Correcting Course
0912
0909
0912
0909
0912
C 155
S 4
C 155
S 4
What is the correcting course and speed to regain track at 0912?
194ºT / 4.2 knots
Set and Drift
Expected set / drift
Correcting Course / Speed
Set: 074T
Drift: 1.4kts

## Slide 73: Correcting Course
0912
0909
0912
0909
0912
C 155
S 4
C 155
S 4
Correcting Course / Speed
Once ordered the correcting course and speed, your ship will regain track at 0912!
Remember, the current is still acting on your ship!!!
194ºT / 4.2 knots

## Slide 74
000°T/003°M
10 kts
1200
1203
1206
1203
1206
1209
Set & Drift
(264° 5 kts)
Compensating
(025°11.6 kts)
Correcting
(041°14.6 kts)
Ordered Course & Speed
Course Made Good Speed Made Good
000°10 kts
334°10.6 kts
1160yds
1460yds
500yds
500yds
Practice
D2
D1
D3

## Slide 75
Enabling Objectives
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
1 - DEFINE Piloting. 2 - DESCRIBE the steps needed to prepare the plotting station. 3 - IDENTIFY the applicable records book needed to record plotting information. 4 - UNDERSTAND how to determine Gyrocompass Error. 5 - IDENTIFY the critical watchstanders needed to transition to restricted waters transit IAW the NAVDORM. 6 - DESCRIBE Visual Fix and demonstrate how a plotter fixes and labels a position using visual NAVAIDs. 7 - DESCRIBE RADAR Fix and demonstrate how a plotter fixes and labels a position using RADAR NAVAIDs. 8 - DESCRIBE COMPOSITE Fix and demonstrate how a plotter fixes and labels a position using both Visual and RADAR NAVAIDs. 9 - DESCRIBE GPS Fix and demonstrate how a plotter fixes and labels a position using GPS. 10 - DESCRIBE Estimated Position and demonstrate how a plotter fixes and labels it. 11 - DESCRIBE Running Fix and its application in piloting. 12 - EXPLAIN the required fix intervals IAW Table 3-A. 13 - DEFINE Dead Reckoning (DR). 14 - IDENTIFY the Six Rules of Dead Reckoning. 15 - DEMONSTRATE how to properly plot and label the course line and DR positions. 16 - DEFINE Set and Drift and demonstrate how to calculate it. 17 - DEFINE Course Made Good (CMG) and Speed Made Good (SMG) and demonstrate how to determine it. 18 - DESCRIBE Compensating Course and demonstrate how to determine it. 19 - DESCRIBE Correcting Course and demonstrate how to determine it.

## Slide 76
Questions?
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy